## Slide 1: Report Presentation
IIT Kanpur
Department of Aerospace Engineering
Dipendra K. Dewangan (241010021)

## Slide 2
Simulation Inputs & Considerations
Reactor Type
Perfectly Stirred Reactor (PSR) model
Steady-state solution
Solve Gas Energy Equation
Operating Conditions
Equivalence Ratio (Φ): 0.6 → 1.3 (continuation, step size = 0.1)
Pressure (P): 1 atm
Reactor Temperature (Initial guess): 1700 K
Inlet Temperature (Tin): 298 K
Residence Time (τ): 0.01 s
Heat Loss (Q): 0 (adiabatic condition)

## Slide 3
Fuel & Oxidizer Definition
Fuel: Ammonia (NH₃)
Oxidizer: Air composition (O₂ + N₂)
  O₂ = 21%
  N₂ = 79%
Complete Combustion Products
H₂O
N₂
Post-Processing Variables Selected
Temperature (K)
Mole fractions of major and minor species:
  NH₃ (unburnt fuel)
  N₂
  O₂
  H₂O
  NO, NO₂, N₂O (NOx emissions)
  OH, H, HO₂, H₂ (radical species)

## Slide 4: φ vs Temperature (K) - flame temp.
Graph 1
Chart: φ vs Temperature (K) - flame temp trend.
| 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3
Temperature_(K) | 1548.382 | 1711.203 | 1842.046 | 1956.118 | 2035.887 | 1995.256 | 1933.528 | 1873.615

## Slide 5: φ vs NO, NO₂, N₂O
Graph 2
Chart: φ vs NO, NO₂, N₂O
| 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3
Mole_fraction_NO_() | 0.0010158 | 0.0024181 | 0.0036944 | 0.0040191 | 0.0020347 | 0.00069582 | 0.00041242 | 0.000296
Mole_fraction_N2O_() | 0.0063564 | 0.0030734 | 0.0011163 | 0.00044432 | 0.00020159 | 0.00013164 | 0.00010954 | 0.00010673
Mole_fraction_NO2_() | 1.3973e-05 | 9.4811e-06 | 4.3809e-06 | 1.7282e-06 | 2.1454e-07 | 3.1266e-08 | 1.7869e-08 | 1.7518e-08

## Slide 6: φ vs NH₃ (unburnt)
Graph 3
Chart: φ vs NH₃ (unburnt)
| 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3
Mole_fraction_NH3_() | 0.002115 | 0.00050411 | 0.00027988 | 0.00024609 | 0.00073952 | 0.0049682 | 0.01167 | 0.020832

## Slide 7: φ vs Radicals (OH, H, HO₂ )
Graph 4
Chart: φ vs Radicals (OH, H & HO₂ )
| 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3
Mole_fraction_H_() | 2.2491e-05 | 4.0799e-05 | 9.1297e-05 | 0.00019358 | 0.00035749 | 0.00042458 | 0.0004265 | 0.00038614
Mole_fraction_OH_() | 0.00036054 | 0.0012169 | 0.0021001 | 0.0025971 | 0.001527 | 0.00051023 | 0.00027209 | 0.00016496
Mole_fraction_HO2_() | 1.8239e-05 | 8.8461e-06 | 4.107e-06 | 1.8596e-06 | 5.8543e-07 | 4.7811e-07 | 5.3423e-07 | 6.4197e-07

## Slide 8: φ vs N₂, O₂ & H₂O
Graph 5
Chart: φ vs N₂, O₂ & H₂O
| 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3
Mole_fraction_N2_() | 0.71662 | 0.70939 | 0.70117 | 0.69278 | 0.68405 | 0.66964 | 0.65478 | 0.64087
Mole_fraction_O2_() | 0.067829 | 0.048217 | 0.030509 | 0.014332 | 0.0033827 | 0.0022196 | 0.0022679 | 0.002631
Mole_fraction_H2O_() | 0.20472 | 0.23439 | 0.25983 | 0.28293 | 0.29908 | 0.29354 | 0.28453 | 0.27583

## Slide 9: φ vs radicals and Nox family gases
Graph 6
Chart: φ vs radicals and Nox family gases
| 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3
Mole_fraction_OH_() | 0.00036054 | 0.0012169 | 0.0021001 | 0.0025971 | 0.001527 | 0.00051023 | 0.00027209 | 0.00016496
Mole_fraction_HO2_() | 1.8239e-05 | 8.8461e-06 | 4.107e-06 | 1.8596e-06 | 5.8543e-07 | 4.7811e-07 | 5.3423e-07 | 6.4197e-07
Mole_fraction_NO_() | 0.0010158 | 0.0024181 | 0.0036944 | 0.0040191 | 0.0020347 | 0.00069582 | 0.00041242 | 0.000296
Mole_fraction_N2O_() | 0.0063564 | 0.0030734 | 0.0011163 | 0.00044432 | 0.00020159 | 0.00013164 | 0.00010954 | 0.00010673
Mole_fraction_NO2_() | 1.3973e-05 | 9.4811e-06 | 4.3809e-06 | 1.7282e-06 | 2.1454e-07 | 3.1266e-08 | 1.7869e-08 | 1.7518e-08
Mole_fraction_NH3_() | 0.002115 | 0.00050411 | 0.00027988 | 0.00024609 | 0.00073952 | 0.0049682 | 0.01167 | 0.020832
Mole_fraction_H_() | 2.2491e-05 | 4.0799e-05 | 9.1297e-05 | 0.00019358 | 0.00035749 | 0.00042458 | 0.0004265 | 0.00038614

## Slide 10: Thank you